## Slide 1
PRE-IDEATHON TEMPLATE
GENESIS
IDEATHON
TEAM & DOMAIN
Introduce your team and the domain you have chosen
Team Name – Actuator Alliance
Team Members – JISHNU PRABU K - CB.EN.U4ECE26018 GAUTHAM V – CB.EN.U4ECE26056, SHARMILI KRISHNAN – CB.EN.U4ECE26014 , PEDIREDLA CHARITESH – CB.EN.U4ECE26063
Selected Domain – 7
Problem Statement – SMART CAMPUS ENERGY MANAGEMENT SYSTEM

## Slide 2: DOMAIN PROBLEM IN OUR WORDS
TEAM
ACTUATOR ALLIANCE
Explain the problem in your domain simply, in your own words
What it exactly solves is In our Campuses often waste a lot of electrical energy because lights, fans, air-conditioner and other electrical systems stay on when rooms are empty or not being used. Most current ways of tracking occupancy and space usage don't give up-, to-date information. This makes it hard to manage energy properly leading to operating costs and wasted power
It is important right now because it MINIMIZES ENERGY WASTAGE in unused campus spaces , LOWERS ELECTRICITY BILLS , it supports sustainability by the reduction of CARBON EMISSION .

## Slide 3: WHO IS AFFECTED?
TEAM
ACTUATOR
ALLIANCE
Who this problem affects and who gains from a fix
Main users: People who run offices, classrooms, labs, hostels and smart homes.
Others involved: Electricity and maintenance teams, security staff, caregivers looking after elderly people, and the people who install IoT systems.
Who gains: The people inside (there is no camera, and an 8x8 thermal image cannot show a face) and the owners (smaller power bills). It is also a small win for the environment by reducing the level of carbon emission.

## Slide 4: CURRENT SITUATION & CONTEXT
TEAM
ACTUATOR
ALLIANCE
How rooms are monitored today
Right now: Lights, fans and AC mostly run on timers, manual switches or basic PIR motion sensors.
Something we noticed: Small mmWave radar and thermal grid modules are now cheap and easy to connect to a microcontroller, but most projects we found use them on their own.
How it works today: The sensor sees movement and switches something on. Nothing checks who or what moved. Or else a camera just records all day.
End result: Empty rooms stay powered, or the lights go off on someone sitting still.

## Slide 5: KEY CHALLENGES
TEAM
ACTUATOR
ALLIANCE
What makes this hard
Main difficulties: PIR cannot see someone sitting still. Radar alone may lose a person who stops moving and cannot tell a person from a pet. A thermal grid alone is only 8x8 pixels.
Why it happens: Each sensor is used by itself, and nothing checks one sensor against the other.
If we ignore it: Energy gets wasted, people get plunged into the dark mid-work, alarms are wrong or missed, users push back on cameras and using cameras were decrease our privacy and it leads to some unwanted problems .

## Slide 6: EXISTING SOLUTIONS / APPROACHES
TEAM
ACTUATOR ALLIANCE
What people already use, and where it falls short
PIR and ultrasonic sensors (Honeywell, Bosch, Panasonic): Cheap and simple, but they don't notice someone sitting quietly and can't tell a person from a dog. Our fix: radar keeps following a person even when they stop moving.
AI cameras (Axis, Hikvision, Google Nest): Very accurate, but nobody likes being filmed, and they use a lot of power and bandwidth. Our fix: an 8x8 thermal grid can't capture a face, so no camera is needed.
mmWave radar alone (Aqara FP2, Hi-Link HLK-LD2450): Great at tracking where people are, but it gets confused by pets and warm objects. Our fix: a thermal check at the spot the radar points to, looking for a human-sized, body-warm blob.
Thermal grid alone (Panasonic AMG8833 Grid-EYE, sold as boards by Adafruit and SparkFun): only 8x8 pixels and no tracking of its own.
Our fix: radar tells it exactly where to look.
Multi-sensor systems: we found them in research and patents, but they rely on cameras and microphones. Ours uses only radar and thermal.
The gap: we couldn't find a low-cost radar + thermal setup, with no camera, that double-checks the exact spot where the radar sees someone.

## Slide 7: PROBLEM INSIGHTS & OPPORTUNITY AREAS
TEAM
ACTUATOR ALLIANCE
What we need to build this
Hardware: an ESP32 board, the HLK-LD2450 mmWave radar (5V, UART), the AMG8833 Grid-EYE thermal sensor (I2C), a power supply, and a relay or LED to show the result.
Sensor range: the LD2450 can track up to 3 people within about 6 m (roughly 120° wide, 70° tall). The AMG8833 picks up body heat up to about 7 m in a 60° view, though we expect it to work best at 3 to 5 m and will test that.
Software: Arduino or ESP-IDF to read the radar targets and thermal frames, Python to log and study the data, simple rules first and then a small classifier (like a decision tree), plus MQTT and a basic dashboard.
Other: test data from different rooms, a few volunteers, a pet and some warm objects (laptop, heater, hot cup), a team split across firmware, fusion and wiring, and guidance from a mentor.

## Slide 8: INITIAL DIRECTION & EXPECTED OUTCOME
TEAM
ACTUATOR ALLIANCE
What we plan to do and what we hope to get
Plan: an ESP32 reads the LD2450 radar all the time. When it sees a target, it reads the AMG8833 at that spot and checks for a human-sized, body-warm blob.
Improve: fewer false alarms from pets, fans and hot objects, and fewer misses on people who sit still, with no camera at all.
Success: "Occupied" shows only for real people, a still person stays counted.
LD2450 Radar
ESP32 Controller
tracks people's x, y and speed
No target
Thermal sensor stays idle
Target detected
Read AMG8833 where radar points
Thermal Analysis
HUMAN
Occupied
ANIMAL
Ignore
OBJECT / HEAT
Ignore
Radar finds where, thermal confirms what

## Slide 9: TEAM CONTRIBUTION
TEAM
Your Team Name
Who will handle which part of the execution
Team Member | Role | Responsibility in Execution
[Member 1 name] | Radar & Firmware | Read LD2450 targets over UART, track people, filter ghost targets
[Member 2 name] | Thermal & Fusion | Read AMG8833, find the heat blob, match radar position to thermal pixels, human / animal / object rules
[Member 3 name] | Hardware | Wiring, 5V power, mounting the two sensors at the same angle, relay or LED output
[Member 4 name] | Testing & Demo | Collect data with people, pets and warm objects, build the dashboard, prepare slides